## Slide 1: Funkcionalna verifikacija hardvera
Predavanje X-XI

## Slide 2: Lecture Content
Monitoring the Verification Flow
  Verification coverage overview
  Structural (code) coverage
  Functional coverage

## Slide 3: Monitoring the Verification Flow
Verification Coverage Overview

## Slide 4: Verification Coverage Overview I
The verification team needs metrics for the quality and completeness of their work as the project proceeds over time.
There are obvious completeness criteria the verification team can derive from the discussions of the verification plan.
Keeping track of the status of different verification tasks is a fundamental piece of information about how well a project is progressing.
Knowledge about which tests the verification engineers have indeed exercised from the test plan provides a necessary metric.
Watching the bug rate is certainly a key piece of scorekeeping that guides a project.
Still, the central question for the verification team remains: “When is verification complete?”
Once the team has finished all planned verification tasks, run all tests, and the bug rate has dropped to zero, is it time to declare success?

## Slide 5: Verification Coverage Overview II
Exhaustive simulation of even small designs is not possible.
The following example shows the combinatorial explosion that makes verification such a daunting task.
Let the DUV be a 16-bit adder. Simulating all combinatorial possibilities of the adder takes 4 billion simulation cycles, assuming that this circuit does not have state-holding elements.
If the project uses a simulation engine that is able to run 1,000 cycles per second, the team still needs around 50 days to simulate this trivial DUV exhaustively.
When does the verification team stop simulation?
Is it good enough to continue until the simulation has been bug-free for 3 days?
How do they know that another day of simulation would not yield yet another bug?
Furthermore, is it truly necessary to simulate the adder DUV exhaustively to make a convincing case of verification completeness?

## Slide 6: Verification Coverage Overview III
It is the task of verification coverage analysis to convince the verification team that they have done sufficient verification, not exhaustive verification, to satisfy defined quality criteria.
Verification coverage is the measurement of state space that simulation-based verification has touched in the entire environment.
Coverage can measure DUV internal states, queues, and activities, as well as DUV inputs and even states of the verification environment components.
Fundamentally, coverage is a measurement of how well the stimulus components have exercised the DUV.
Coverage cannot make a statement on the quality or robustness of the checking components.

## Slide 7: Verification Coverage Target Areas I
There are two completely complementary sides of the verification coverage task.
First, there is coverage of the verification environment.
Here, the objective is to measure how well the verification stimulus environment covers the specification of the design.
This coverage aspect is called verification test coverage.
Second, there is coverage of the function implemented in the DUV.
This metric seeks to measure how well the verification stimulus activates or exercises the implementation of the specification in the concrete design.
This coverage task is called implementation coverage.
Figure on the right shows the two areas of coverage analysis side by side.

## Slide 8: Verification Coverage Target Areas II
The base activity that precedes any type of coverage analysis is the collection of coverage measurements.
The verification team collects the measures for test coverage from the stimulus initiator component, the test case, or the interface into the DUV.
Implementation coverage analysis relies on measurements of activities inside the DUV by inspection into the HDL model during simulation.
Throughout the measurement and analysis activity, the verification team must never forget that the ultimate goal of coverage analysis is to guide the verification process, and not to prove its completeness.
Completeness is an elusive goal that is unreachable anyway.

## Slide 9: Verification Coverage Goals I
A seemingly simple coverage goal would be the combinatorial space spanned by the enumeration of all possible patterns on the DUV inputs, all possible states internal to the DUV, and all possible output patterns on the outputs of the DUV.
Although this coverage metric is trivial to define, it is also completely useless to guide the verification process, because it is unachievable.
Then, toward which targets should coverage analysis drive the verification process?
Coverage analysis could be defined as the task to maximize the probability of stimulating and detecting bugs, at minimum cost (in time, labor, and computation).
In the end, not very surprisingly, detection of hidden bugs is the main objective of the verification process.

## Slide 10: Verification Coverage Goals II
Figure on the right illustrates how coverage information can guide the simulation through the state space of a DUV to find the hidden bugs.
The generated stimulus drives the simulation through the state space in a meandering path.
The task of coverage guidance is to influence the direction of the traversal to hit areas that are prone to hidden bugs.
In summary, the amount of hidden bugs found measures the quality of the coverage analysis effort.
Coverage is a tool that helps the verification team to find bugs, and it is only a means to an end.
A coverage measure that the verification team meets without finding bugs has only a limited value.
Several times it has been said that it is impossible to cover all parts of a design with simulation.
Therefore, coverage must focus on error prone areas.
In this sense, a good coverage metric needs to have a predictive component; it needs to be able to measure bug coverage.
Verification coverage guidance to the hidden bugs. The overall rectangle represents the state space of a design under verification (DUV). Simulation traverses through this state space along a zig-zag trajectory. The hidden bugs in the DUV are shown as shaded circles. Influence of coverage guidance is shown by arrows that cause the simulation traversal to change in a different direction, hopefully closer to a hidden bug.

## Slide 11: Verification Coverage Models
Figure on Slide 7 distinguishes coverage efforts by their target areas - test coverage versus implementation coverage.
Developers and researchers have evolved different successful schemes to specify coverage metrics for both applications.
These schemes are referred to as coverage models.
It is possible to classify coverage models as either structural (code) or functional. Both classes apply to verification test coverage or implementation coverage.
Functional coverage models focus on the semantics of either the test or the design implementation.
For example, did the test cover all possible commands or did the simulation ever trigger a first in, first out (FIFO) buffer overflow?
Structural (code) coverage models, on the other hand, tie into the representation of the domain to be covered.
A good example for a structural coverage model is line coverage, a measure of whether all source lines in the stimulus generator program or the DUV HDL have been visited during simulation.

## Slide 12: Monitoring the Verification Flow
Structural (Code) Coverage

## Slide 13: Structural (Code) Coverage
The application for structural coverage models is largely implementation coverage analysis.
These models always tie into a structural aspect of the implementation of the test generation, the DUV, or the representation of the design HDL.
We will review the most common structural coverage measures:
  toggle,
  line‚
  statement‚
  branch‚
  path,
  condition and
  FSM coverage.

## Slide 14: Toggle Coverage
Toggle coverage measures how many times the signals and latches (facilities) in the HDL model have changed their logic value during simulation.
The absence of signal change activity in an area of the DUV indicates that the stimuli did not target this area at all.
The advantage of toggle coverage is that it is a very simple, easy-to-understand model.
Its drawback is, however, that it yields massive amounts of data, and the statement that 100% of all signals in a DUV have toggled does not yield any insight into the functional significance of the testing done.
Example of the toggle coverage for the 11-bit reg signal is shown on the figure to the right.
Some code coverage tools report not only zero-to-one and one-to-zero transitions‚ but also transitions to and from undefined (“X”) and tristate (“Z”).
Toggle Coverage Example

## Slide 15: Line Coverage
Line coverage takes the syntactical structure of the HDL specification and measures which HDL lines were executed by the simulation run.
Similar to toggle coverage, this coverage model is easy to comprehend, and the absence of activity in areas of the HDL model highlights omissions in the tests.
The limitation of line coverage is the missing semantic insight.
The fact that an HDL statement has been executed results in no knowledge about the correctness of the content of the statement.
Line Coverage Example
Notes: A related coverage metric reported by some tools‚ block coverage‚ defines a sequence of statements with no branches to be a block. (A branch is introduced by any control flow statement such as an “if” or “while” statement). If the first statement of the block is executed‚ all of the statements in the block are executed. Although block coverage offers the same visibility into RTL execution as line coverage‚ less overhead is introduced during simulation because only one counter is inserted per block.

## Slide 16: Statement Coverage
Statement coverage reports which RTL statements have and have not been executed.
This metric is more precise than line coverage because statements may span multiple lines and more than one statement may occupy a single line.
Statement Coverage Example

## Slide 17: Branch Coverage
Branch coverage or conditional coverage looks at conditional statements (if‚ case‚ while‚ repeat‚ forever‚ for and loop) in the HDL and keeps track of which conditions the simulation encounters and which it does not.
This model assumes that there is semantic meaning in the condition that the designer expressed in HDL.
Decision points in the HDL specification are typically representative of different conditions to which the design needs to react.
Therefore, the lack of exercising a decision in all possible, anticipated ways clearly indicates a lack of testing.
Branch Coverage Example

## Slide 18: Path Coverage
Path coverage is a refinement of branch coverage. Path coverage reports the number of times every possible path through the code was executed.
Rather than looking at single conditional decisions in isolation, path coverage does an execution flow analysis of the HDL and identifies combinations of subsequent decisions into execution paths.
Figure to the right shows the automatic inference of four possible execution paths on a given HDL with if/then/else structure.
If branch coverage would have been used, it would indicate that all branches were taken.
But, only the path coverage could reveal that one of the possible paths through the structure has not been taken, which could be significant indication for the verification team.
Path Coverage Example

## Slide 19: Condition Coverage
Condition coverage records the number of times each permutation of the terms of a Boolean expression cause the complete expression to evaluate to true or false.
Consider the expression (A && B) || C || D. This expression evaluates to true under three conditions:
  1. A && B
  2. C
  3. D
and to false under two conditions:
  1. !A && !C && !D
  2. !B && !C && !D
A stricter form of condition coverage - exclusive condition coverage - is sometimes available that requires each term to be the controlling term (i.e. sole reason) for an expression to evaluate true or false.
For the example above, the expression evaluates to true for these five exclusive conditions. The controlling term is in boldface below:
  1. A && B && !C && !D
  2. !A && B && C && !D
  3. A && !B && C && !D
  4. !A && B && !C && D
  5. A && !B && !C && D

## Slide 20: FSM Coverage Example – State Coverage
Consider the following FSM composed of five states and nine arcs shown on the figure to the left. Next to each arc is its next-state equation.
State coverage for this FSM might be reported as in figure to the right.
State Coverage

## Slide 21: FSM Coverage Example – Arc Coverage
Arc coverage for the same FSM might be reported as in figure to the right.
Arc Coverage

## Slide 22: FSM Coverage Example – Sequential Arc Coverage
Lastly, sequential arc coverage, for two-arc transitions beginning at state S1, for the same FSM might be reported as in figure to the right.
Sequential Arc Coverage

## Slide 23: Monitoring the Verification Flow
Functional Coverage

## Slide 24: Functional Coverage I
The purpose of measuring functional coverage is to measure verification progress from the perspective of the functional requirements of the device.
The functional requirements are imposed on both the inputs and outputs of the device - and their interrelationships - by the device specifications (functional specification and design (microarchitecture) specification).
The input requirements dictate the full data and temporal scope of input stimuli to be processed by the device.
The output requirements specify the complete set of data and temporal responses to be observed.
The input/output requirements specify all stimulus/response permutations which must be observed to meet black-box device requirements.
Since the full behavior of a device may be defined by these input, output and input/output requirements, a functional coverage space which captures these requirements is referred to as a coverage model.
The degree to which a coverage model captures these requirements is defined to be its fidelity.
The fidelity of a model determines how closely the model defines the actual behavioral requirements of the device. This is the abstraction gap between the coverage model and the device.
Notes: For example, if we are modeling a control register having 18 specified values and the coverage model defines all 18 values, their is no abstraction gap so this is a high fidelity model. However, if a 32-bit address bus defines all 232 values and an associated coverage model groups those values into 16 ranges, a substantial abstraction gap is introduced. Hence, this would be a lower fidelity model.
In addition to the abstraction gap between the coverage model and the device, another source of fidelity loss is omitting functional relationships from the model. For example, if two bits, such as CR3 and CR7 of the control register, have a dependency such as “CR3 may only be one if CR7 is one”, yet this dependency is not reflected in an associated coverage model, that model is of a lower fidelity than a model that captures this relationship.

## Slide 25: Functional Coverage II
Unlike structural coverage, there is no automated way to create functional coverage models.
Functional coverage targets semantic aspects of the test generation or design implementation.
Underlying all functional coverage activities there is the acknowledgement that it is necessary to choose which functional areas of the design need to be tested.
Insight into the design semantics drives these choices, and they must come from the designer or the verification engineer.
A very important component of this insight is the knowledge of design complexity, of areas that are prone to bugs.
The predictive bug coverage component of functional coverage models must come from the experience of the engineers.
There is no set of complex automation tools available to define functional coverage models.
The tool support focuses mostly on the implementation of the coverage model and the efficient collection of the data during runtime. After the data are collected, the tools provide GUI support to help in the traversal of the results.

## Slide 26: Functional Coverage Model Designing Steps
Functional coverage model design steps include:
  describing the semantics of the model,
  identifying the coverage attributes (events) and
  specifying the relationships among these attributes which characterize the device and time when to correlate them.
The semantics of the model is an English description of what is modeled, sometimes called a story.
An example for an input coverage model is:
  The instruction decoder must decode every opcode, in every addressing mode with all permutations of operand registers.
An output model example is:
  We must observe the packet processor write a sequence of packets of the same priority, where the sequence length varies from one to 255.
Once the semantic description is written, the second step in designing a coverage model is identifying attributes, or as it is sometimes called, coverage events. But first, what is meant by an attribute?
An attribute specifies an event in the model or the test bench, which is important enough that the verification environment must note and log its occurrence.
An attribute identified from one of the device specifications is a parameter of the device such as configuration mode, instruction opcode, control field value or packet length.

## Slide 27: Matrix Coverage Model
A matrix model considers each attribute to be a dimension of a matrix, where the number of dimensions is defined by the number of attributes.
The values along each axis are the values of the corresponding attribute.
Figure to the right illustrates a two dimensional matrix model.
The two attributes are labeled “Attribute A” and “Attribute B.”
Attribute A has twelve values, A0 through A11 while attribute B has eight values, B0 through B7.
An attribute pair, (An, Bm), defines a point within this two dimensional coverage space.
This matrix model defines 96 points.
Matrix Coverage Model

## Slide 28: Hierarchical Coverage Model
A hierarchical model is structured like an inverted tree with its root at the top.
It is a directed graph whose nodes are attribute values and whose edges indicate a relationship between one attribute value and another.
One attribute is represented at each level in the tree, with the primary controlling attribute at the root and each successive attribute one level lower.
Figure to the right illustrates a hierarchical coverage model defined by three attributes: “Attribute A,” “Attribute B” and “Attribute C.”
Attribute A is the primary controlling attribute and has four values, A0 through A3.
Attribute B is a secondary attribute and has three values, B0, B1 and B2.
Attribute C is a tertiary attribute having four values, C0 through C3.
In this model, an attribute 3-tuple, (An , Bm , Ck), defines one of the ten points in the coverage space.
For example, p7 is defined by (A2, B0, C2), the path to this point.
Hierarchical Coverage Model

## Slide 29: Hybrid Coverage Model
A hybrid model is composed of a blend of matrix and hierarchical regions, where fully permuted attribute combinations are structured as a matrix and irregular attribute relationships are structured hierarchically.
The matrix subregions may be leaf nodes of a base hierarchical model or hierarchical subregions may occupy nodes within a base matrix model.
Figure on the right illustrates a hybrid model of the first type, matrix subregions are leaf nodes of a base hierarchical model.
Attributes A, B and C are defined the same as the previous hierarchical model, having four, three and four values respectively.
Attribute D has three values, D0, D1, and D2 and attribute E has six values, E0 through E5. These two attributes define a three by six matrix subregion of the hierarchical model.
Attributes F and G likewise define a five by four matrix subregion.
This model defines a total of 46 points: 8 leaf nodes (p1, p3, p4, p5, p6, p7, p8, p9), 18 points in the attribute D/E matrix and 20 points in the attribute F/G matrix.
Hybrid Coverage Model

## Slide 30: Pros and Cons of Each Model I
Although the structure of the coverage model should reflect the underlying relationships among the attributes from which it is composed, there are times when the relationships may be modeled using more than one of these model structures.
What are the pros and cons of each structure in terms of model fidelity and implementation effort?
The matrix model requires the least effort to design and implement because of its symmetry. Each of the interacting attributes is specified, along with its corresponding values.
Because the matrix model is so easy to build, engineers often choose it as the path of least resistance even though another model is more applicable.
If the full size of a model, structured as a matrix, is relatively small (1,000 points or less) and the most of the coverage points are not invalid or impossible to reach, the time saved over designing a more precise hierarchical or hybrid model is worth the loss of fidelity.
However, if the matrix model would be quite large (100,000 or more points) or it would define many invalid points, a hierarchical or hybrid model should be chosen instead.

## Slide 31: Pros and Cons of Each Model II
The hierarchical model requires more effort to design because, not only must the attributes and their values be specified, specific relationships among attributes must also be defined.
These relationships are often quite irregular and complex, requiring many lines to enumerate.
Nonetheless, the complexity reflected in the hierarchical model is inherent in the attribute relationships described by the device specification or reflected in the RTL implementation. Although it may be simplified using a lower fidelity model, it cannot be avoided.
The strength of the hierarchical model is that it can precisely define attribute relationships, dramatically reducing the size of a coverage model and providing deeper insight into observed device behaviors.

## Slide 32: Pros and Cons of Each Model III
The hybrid model requires a design effort comparable to the hierarchical model.
Again, attributes, values and individual relationships must be enumerated.
However, some regions of a hybrid model are quite regular and are represented by a matrix structure.
The hybrid model usually reflects the most precise input, output or internal device behavior because of the nature of designs.
They are a blend of symmetric values with a few exceptions tossed in.

## Slide 33: Detailed Design
Detailed design concerns itself with mapping the coverage model design to the verification environment.
In other words, how must the design be architected so that it may be implemented in VHDL?
In order to answer the question, three specific questions must be answered:
  1. What must be sampled for the attribute values?
  2. Where in the verification environment should we sample?
  3. When should the data be sampled and correlated?
The answer to the first question maps verification environment fields and variables, or device signals and registers, to attributes.
The answer to the second question determines where in the verification environment data sampling will be performed.
The answer to the third question maps the sampling and correlation times to specific events in the environment.

## Slide 34: What to Sample
The data to be captured for each of the attributes defined during functional coverage model design must be associated with a data source in the environment, either in the verification environment or in the device under verification.
For example, the attributes of an input coverage model will be sampled from data injected into the device.
The attributes of output coverage model will be sampled from data captured on device outputs.
Some coverage models may require attributes that may only be captured from within the DUV or may compose attributes from all three sources.

## Slide 35: Sampling Input Attributes
Input attributes should be sampled by a monitor that has access to the primary inputs to the device.
The monitor should sample data from input signals at valid times specified by the device specification.
The monitor should not retrieve its data from a stimulus generator because creating such a dependency would compromise the ability to reuse the monitor for recording coverage at a subsequent integration level
The figure on the right depicts a monitor sampling data from a device’s primary inputs.
The block labeled “Coverage” is a distinct aspect from the “Input Monitor” block because it has a particular responsibility whereas the monitor is more general-purpose.
The coverage block is solely responsible for recording functional coverage data.
The monitor block is a generic data capture facility, used by both coverage and checking aspects.
Sampling Input Attributes

## Slide 36: Sampling Output Attributes
Output attributes should also be sampled by a monitor but, of course, from the primary outputs of the device.
The monitor should sample data at valid times specified by the device specification.
The figure on the right depicts a monitor sampling data from a device’s primary outputs.
Sampling Output Attributes

## Slide 37: Sampling Internal Attributes
Device internal attributes also have an associated monitor, responsible for capturing internal signal and register values.
Unlike the input and output interfaces of the device, internal signals are not as well specified (if they are specified at all).
Sampling of such internal signals must be coordinated with the design team in order to minimize volatility.
Because internal signals may be quite volatile and are frequently unspecified, the use of internal attributes for coverage model design should be minimized.
They impose an additional maintenance burden on the verification team, once implemented, because the monitor and coverage must continually track design changes.
One strategy that was successfully employed to address this is defining a set of fixed signals and registers for verification use.
The verification team identifies internal signals and registers required for coverage measurement and the design team agrees to minimize their changes.
This “verification interface” is treated the same as an external device interface because it is specified and (nearly) frozen.
The bottom figure depicts a monitor sampling data from the DUV’s internal signals and registers.
Sampling Internal Attributes

## Slide 38: Coverage Model Example – Calc1 Design
During the verification of the Calc1 the driver should generate all commands, including illegal ones, at least once for every port. To monitor this we can design the following coverage model.
First we must identify the coverage attributes (events). Our coverage model will have two attributes:
  First attribute is the port to which the command is issued. Possible values for this attribute are 1, 2, 3 and 4.
  Second attribute is the command type with the possible values “No operation”, “Add”, “Subtract”, “Shift left”, “Shift right”, “Illegal”
  Since all attribute combinations are legal, we will use the matrix coverage model, as shown on the figure below shows.
Sampling times for both attributes equal the system clock period. Correlation time should be equal to the system clock period also.
The goal to cover all cells of the cross-product is equivalent to the statement that the driver generated all commands, including illegal ones, at least once for every port.
Matrix coverage model for Calc1 stimulus.
The two dimensions of the matrix are operations and ports. The coverage model gives insight into which operation/port combinations were not simulated versus which ones were and how many times they were simulated.

## Slide 39: Analyzing the Collected Coverage
It is possible to analyze the collected coverage data per test case. Alternatively, the coverage collection tool can tabulate many test case results into one result.
Coverage tools typically provide two types of reports: status reports and progress reports.
The status report, Figure (a), shows the current overall encountered coverage events in a snapshot diagram, whereas the progress reports, Figure (b) display a curve of the increasing sum of encountered events over the process of test case simulation.
The typical shape of the progress is asymptotical toward the goal of reaching all events, with a sharp increase in the beginning of the process.
The early events are typically the easy ones to hit, whereas the events encountered later need much more effort from the verification team, tuning the stimulus generation.
Coverage reports.
(a) Status report showing the summary of all coverage data up to a point in time.
(b) Coverage results tabulated over time.